5.0mm Round Type LED Lamp

- Features :

- Choice of various viewing angles

- Available on tape and reel.

- Reliable and robust

- Pb free

- The product itself will remain within RoHS compliant version.

- Descriptions :

- The series is specially designed for

applications requiring higher brightness

- The led lamps are available with

different colors, intensities.

- Applications:

- TV set

- Monitor

- Telephone

- Computer

| PART NO. | Material | Emitting Color | Lens Color |
| --- | --- | --- | --- |
| 523SUBC | InGaN | Super Ultra Blue | Water Clear |

- Packing Dimensions & Spatial Distribution:

| Product Model | Emitting Color | LENS | DIE Material |
| --- | --- | --- | --- |
| 523SUBC | Super Ultra Blue | Water Clear | InGaN |
| Tolerance Grade | Dimension Tolerance (UNIT: mm Tolerance ) |
|  | 0.5~3 | 3~6 | 6~30 | 30~120 |
| Medium(m) | ±0.1 | ±0.2 | ±0.3 | ±0.5 |

2. Absolute Maximum Ratings: (TA=25℃)

| Parameter | Symbol | Color | Maximum Rating | Unit |
| --- | --- | --- | --- | --- |
| Peak Forward Current | IFp | Blue | 70 | mA |
| Forward Current | IF | Blue | 20 | mA |
| Reverse Voltage | VR | Blue | 5 | V |
| Power Dissipation | Pd | Blue | 100 | mW |
| Operating Temperature | Topr | Blue | -40 ~ +85 | ℃ |
| Storage Temperature | Tstg | Blue | -40 ~ +85 | ℃ |
| Electrostatic Discharge | ESD | Blue | 1000 | V |
| Soldering Temperature | 260℃ for 5 seconds |

Notes:

1. Absolute maximum ratings Ta=25℃.

2. Tolerance of measurement of forward voltage±0.1V.

3. Tolerance of measurement of peak Wavelength±2.0nm.

4. Tolerance of measurement of luminous intensity±15%.

5. Tolerance of measurement of angle intensity±15%.

# Text boxes

ATTENTION

OBSERVE PRECAUTIONS

FOR HANDLING

ELECTROSTATIC

SENSITIVE DEVICES